## Slide 1
CRUSHIT
Gamified Pedal Can Crusher · Urban Recycling Reimagined
IMechE CADathon 2026 · SDG 11: Sustainable Cities & Communities
▼

## Slide 2
THE PROBLEM
Aluminium cans: valuable, recyclable and constantly dumped in the wrong bin
~2.5×
more cans
fit when they are crushed
75%
of aluminium ever made
is still in active use today
95%
energy saved recycling
aluminium compared to smelting it raw
Root cause: Recycling bins are inconvenient, passive, and boring. People skip them especially at events like football matches where waste peaks. CrushIt makes the right choice the fun choice.

## Slide 3
OUR SOLUTION
CrushIt: A pedal-powered, gamified aluminium can crusher bin
⚡
Zero electricity
Entirely foot-pedal driven. No battery, no grid connection needed.
♻️
Compact crushing
Reduces can volume by approx. 60%. 2.5× more cans per collection cycle.
🎮
Gamified engagement
Dual-sided crusher: pick Team A or B to answer trivia/vote. Count tracked live. Fun for all ages.
🔒
Safety-first design
Manual lid closure before pedal activates. Finger entrapment possibility eliminated.
💧
Liquid waste capture
Grid lower platform drains residual liquid to sealed tray. Thus, clean crushes and no mess.
⚽ STADIUM CRUSHIT
Messi 🆚 Ronaldo
Who gets more cans? Pick a side!
🔴
Side A
505
cans
🔵
Side B
470
cans
Crush your can. Cast your vote.

## Slide 4
CAD & ENGINEERING DESIGN
1
Foot Pedal Actuation
Pedal drives a 2-hinge toggle linkage, converting foot force to vertical platform travel.
2
Upper Fixed Platform
Spike on punctures can top on contact to releases pressure & drain residual liquid before full crush, mitigating explosion caused by carbonation.
3
Lower Moving Platform
Grid-pattern base travels upward to crush the can. Open grid allows liquid to drain into sealed collection tray below.
4
Slanted Floor + Exit Slot
Floor slightly inclined toward a side slot at base. After crushing, the can slides on to the collection tray.
5
Safety Lid + Pedal Lock
User manually closes lid before use. Mechanical interlock prevents pedal from actuating until lid is fully shut.

## Slide 5
MATERIALS & COST VIABILITY
Component | Material | Justification | Est. Unit Cost
Crushing platforms | 304 Stainless Steel | Corrosion-resistant, food-safe, high compressive strength | £15 – 25
Housing enclosure | HDPE (injection moulded) | Weatherproof, lightweight, recyclable; low cost for long life cycle. | £8 – 20
Hinge linkage | Galvanised mild steel | High fatigue life for high-cycle repetitive loading | £5 – 10
Liquid tray | Polypropylene (PP) | Chemical-resistant, food-grade, easy to injection mould | £3 – 6
Puncture spike | Hardened stainless steel | Puncture resistance, hygiene compliance, corrosion-free | £2 – 4
Manufacturing at Scale
HDPE injection moulding – enclosure ~£0.80–2.00/unit at volume
Sheet metal stamping – platforms: precise & repeatable
Estimated total unit cost: £55–100 at scale
SDG 11 Alignment
✓ Cuts bin contamination and landfill waste
✓ 2.5× bin capacity → fewer collection vehicles
✓ Passive design — zero ongoing energy use
✓ All materials recyclable at end-of-life

## Slide 6
FUTURE DEVELOPMENT & IMPACT
👁️
Finger-Safety IR Sensor
IR sensor detects hands inside crush zone. Auto-locks pedal until clear of hands. More Convient.
📊
Live Digital Display
LED panel shows crush count, bin fill %, and live game scores. Low power draw. Drives competition and repeat engagement.
🛒
Vending Machine Pairing
Pair CrushIt units adjacent to beverage vending machines. Deposit tokens dispensed per crush for discounts.
📡
Fill-Level Monitoring
Smart sensors report bin fill to council waste teams. Eliminates unnecessary collections, optimising routes.
CrushIt — making recycling something people actually want to do.